## Slide 1
T
Reducing GHG Emissions in Canada: A Formidable Challenge
Trottier Energy Futures Project Results
Presented by Dr. John Leggat
5 April 2016

## Slide 2: Background
IPCC – “There are multiple pathways to… significantly reducing GHG emissions”
Canadian situation presents unique challenges and opportunities
TEFP – Study sponsored by CAE and DSF. Funding from Trottier Family Foundation
Rigorous and comprehensive engineering analysis
Results suggest pathways and enablers; not solutions
Stimulate informed discussion

## Slide 3: A Significant Undertaking
Goal of 80% reduction in GHG emissions by 2050 compared to 1990 levels – 118Mt
Options and pathways for reducing GHG emissions by more than 100% by 2100
Combustion and non-combustion emissions
Alternate Futures analysis
Medium Term (2030) – promising pathways
Long Term (2050) – hard problems

## Slide 4: Emissions - Mt
Year | Total | Combustion | Non-Combustion
TARGET | 118 |  | 
1990 - actual | 591 | 427 | 164
2010 - actual | 692 | 498 | 194

## Slide 5: Approach to the Analysis
NATEM Model –
Linear programming optimization model
Primary drivers are end-use demands
Long-term horizon (50-100 years)
GHG emission targets
CanESS Model –
Simulation model
Primary drivers are demographic and macro-economic dynamics
All scenarios executed in 1-year steps
Tracks GHG emissions at the sources

## Slide 6
Technology Change
Behavioural/Social Change
3
4
5
8
1
Approach to Analysis
Alternate Futures Scenarios
8a
3a

## Slide 7: 1990 Emissions 591 Mt
Chart: 
| Agriculture | Commercial | Residential | Industrial | Transport | Electricity | Fossil fuel production | Agriculture processes | Industrial processes | Fugitive emissions | Other
1990 | 2.3912 | 25.6994 | 43.4894 | 57.6855 | 146.1814 | 93.6119 | 57.7638 | 46.7285 | 45.2802 | 42.3636 | 19.0074

## Slide 8: Energy Utilization
Other Hydrogen Biomass Electricity Fossil Fuel

## Slide 9: Reference Scenario 1 – Present Policies 1109 Mt in 2050
Chart: 
| Agriculture | Commercial | Residential | Industrial | Transport | Electricity | Fossil fuel production | Agriculture processes | Industrial processes | Fugitive emissions | Waste
2050 | 18.0457 | 36.4948 | 54.8465 | 114.6061 | 244.8358 | 72.9085 | 212.5985 | 87.9 | 118.5939 | 97.9462 | 34.1328

## Slide 10: Scenario 8a – 60% Target 394 Mt in 2050
Chart: 
| Agriculture | Commercial | Residential | Industrial | Transport | Electricity | Fossil fuel production | Agriculture processes | Industrial processes | Fugitive emissions | Waste
2050 | 5.9915 | 4.6293 | 5.4097 | 37.37 | 90.8331 | 0.57161 | 25.7623 | 74.715 | 118.5939 | 12.8883 | 17.0664

## Slide 11: Combustion Emission Reductions Scenario 8a (70% reduction – 128 Mt)
Chart: Mt CO2-eq
| 2011 | 2013 | 2020 | 2030 | 2040 | 2050
Agriculture | 15.0907 | 15.5939 | 16.7515 | 11.7679 | 8.159 | 5.3105
Commercial | 36.5107 | 36.5429 | 33.9101 | 26.3491 | 12.055 | 3.6198
Electricity | 87.0758 | 77.9363 | 37.046 | 1.1269 | 0.75227 | 0.43366
Industrial | 53.6408 | 53.5198 | 58.4751 | 58.5149 | 44.8964 | 34.3319
Residential | 43.4839 | 43.4806 | 39.2239 | 27.9827 | 14.7121 | 4.4774
Supply | 106.2639 | 107.0348 | 87.4923 | 72.7274 | 50.5543 | 18.579
Transportation | 169.8804 | 167.1578 | 167.1011 | 136.531 | 98.8709 | 61.3174
S8a - 70% reduction | 511.9461 | 501.2662 | 440 | 335 | 230 | 128.0697
Fossil fuel production

## Slide 12: Emissions - Mt
Year | Total | Combustion | Non-Combustion
TARGET | 118 |  | 
1990 - actual | 591 | 427 | 164
2010 - actual | 692 | 498 | 194
2050 - no change | 1109 | 755 | 354
2050 – 60% | 394 | 171 | 223
2050 – 70% | 351 | 128 | 223

## Slide 13: Cost per Tonne of CO2 Reduction

## Slide 14: Principal Observations
Reduction pathways result in major end use changes
Largest reduction is 70% for combustion emissions
Non-combustion emissions need attention
Infrastructure availability projections are optimistic
Challenge to achieve 80% reduction by 2050
Net negative emissions required before 2050
Immediate priorities are clear; longer term path requires more investigation and research

## Slide 15: Promising Pathways
Absolute importance of carbon free electricity
Best sources of electricity are hydro, nuclear and wind
Interjurisdictional transfers of electricity and access to storage are important
Considerable infrastructure investment is needed quickly
Reduced dependency on fossil fuels means lifestyle changes

## Slide 16: Hard Problems
  Heavy road and rail transportation
  Insufficient feedstock to meet demand for biofuels
  Process changes for oil and natural gas are needed
  Changing urban form and behaviour – how will it be done in a North American context?
  Non-combustion emissions
  Net negative emissions
  Very fast build of large infrastructure required.

## Slide 17: Immediate Priorities
Energy conservation / energy efficiency
Electrification of end uses
Decarbonizing electricity supply
Major growth and changes to electricity supply system
Research and development for hard problems

## Slide 18: Opportunities
Low cost and carbon-free electricity - industrial production and export
Export of dependable capacity and electricity to U.S. and provision of storage
Expansion of forestry and agricultural sectors for production of biomass / biofuels
Carbon retention in wood products
Changes in petroleum sector for reduced emissions
Environmental and societal equilibrium

## Slide 19: Contributions from The Trottier Energy Futures Project
Provides perspectives on different pathways for deep GHG reductions
Demonstrates scale and complexity of the challenge
Defines where to start
Highlights hard problems
Identifies opportunities for immediate action
Shows merits of analytical approaches and need for sustaining and growing these capabilities

## Slide 20
The full report
and executive summary
are available at:
http://iet.polymtl.ca/tefp
We welcome your comments:
iet@polymtl.ca